## Slide 1: Capacitance & Dielectrics
Definition of capacitance
Calculating capacitance of capacitors with simple geometries
Combination of capacitors
Circuit symbols to represent capacitors connected to batteries
Energy stored in a charged capacitor
Capacitors with dielectrics
Introduction

## Slide 2: Circuits and Circuit Elements
Electric circuits are the basis for the vast majority of the devices used in society.
Circuit elements can be connected with wires to form electric circuits.
Capacitors are one circuit element.
  Others will be introduced in other chapters
Introduction
Capacitors
Capacitors are devices that store electric charges.
Examples of where capacitors are used include:
  radio receivers
  filters in power supplies
  to eliminate sparking in automobile ignition systems
  energy-storing devices in electronic flashes

## Slide 3: Makeup of a Capacitor
A capacitor consists of two conductors.
  These conductors are called plates.
  When the conductor is charged, the plates carry charges of equal magnitude and opposite signs.
A potential difference exists between the plates due to the charges.
Section 26.1

## Slide 4: Definition of Capacitance
The capacitance, C, of a capacitor is defined as the ratio of the magnitude of the charge on either conductor to the potential difference between the conductors.
The SI unit of capacitance is the farad (F).
The farad is a large unit, typically you will see
microfarads (μF) and picofarads (pF).
Capacitance will always be a positive quantity.
The capacitance of a given capacitor is constant.
The capacitance is a measure of the capacitor’s ability to store charge.
  The capacitance of a capacitor is the amount of charge the capacitor can store per unit of potential difference.
Section 26.1

## Slide 5: Parallel Plate Capacitor
Each plate is connected to a terminal of the battery.
  The battery is a source of potential difference.
If the capacitor is initially uncharged, the battery establishes an electric field in the connecting wires.
This field applies a force on electrons in the wire just outside of the plates - > electrons moving onto the negative plate - > continues until equilibrium is achieved: plate, wire & terminal at the same potential.
At this point, there is no field present in the wire and the movement of the electrons ceases - > plate negatively charged; A similar process occurs at the other plate.
In its final configuration, the potential difference across the capacitor plates is the same as that between the terminals of the battery.
Section 26.1

## Slide 6: Capacitance – Parallel Plates
The charge density on the plates is σ = / A.
  A is the area of each plate, the area of each plate is equal
  is the charge on each plate, equal with opposite signs
The electric field is uniform between the plates and zero elsewhere.
The capacitance is proportional to the area of its plates and inversely proportional to the distance between the plates.
Section 26.2

## Slide 7: Capacitance - Cylindrical Capacitors (Optional)
Section 26.2
From Chapter 24

## Slide 8: Capacitance - Spherical Capacitor (Optional)
Section 26.2
From Chapter 24

## Slide 9: Capacitance – Isolated Sphere (Optional)
Assume a spherical charged conductor with radius .
The sphere will have the same capacitance as it would if there were a conducting sphere of infinite radius (), concentric with the original sphere.
Assume for the infinitely large shell
Note, this is independent of the charge
on the sphere and its potential.
Section 26.2
From previous page

## Slide 10: Circuit Symbols
A circuit diagram is a simplified representation of an actual circuit.
Circuit symbols are used to represent the various elements.
Lines are used to represent wires.
The battery’s positive terminal is indicated by the longer line.
Section 26.3

## Slide 11: Capacitors in Parallel
Section 26.3
The potential difference across the capacitors is the same.
And each is equal to the voltage of the battery
  DV1 = DV2 = DV
  DV is the battery terminal voltage
The total charge is equal to the sum of the charges on the capacitors.
  Qtot = Q1 + Q2

## Slide 12: Capacitors in Parallel (Equivalent capacitance)
ΔV1 = ΔV2 = ΔV
Qtot = Q1 + Q2
Qtot = Q1 + Q2
= C1DV1 + C2DV2
= C1DV + C2DV
Therefore,
Ceq = Qtot /DV = C1 + C2
Section 26.3
Ceq = C1 + C2 + C3 + … (parallel combination)
Equivalent to
The capacitors can be represented by one capacitor with a capacitance of Ceq.

## Slide 13: Capacitors in Series
Section 26.3
The potential differences (DV1 and DV2) across the capacitors are NOT the same.
The total potential is
  DV = DV1 + DV2
The charge on each capacitor is same.
  Q1 = Q2 = Q

## Slide 14: Capacitors in Series (Equivalent capacitance)
Section 26.3
Q1 = Q2 = Q
ΔVtot = ΔV1 + ΔV2
Q/Ceq = ΔVtot = ΔV1 + ΔV2 = Q1/C1 + Q2/C2
Therefore,
1/Ceq = 1/C1 + 1/C2
(series combination)
The capacitors can be represented by one capacitor with a capacitance of Ceq.
Equivalent to

## Slide 15: Equivalent Capacitance, Example
The 1.0-mF and 3.0-mF capacitors are in parallel.
The 6.0-mF and 2.0-mF capacitors are in parallel.
These parallel combinations are in series with the capacitors next to them.
The series combinations are in parallel and the final equivalent capacitance can be found.

## Slide 16: Energy in a Capacitor – Overview
Consider the circuit to be a system.
Before the switch is closed, the energy is stored as chemical energy in the battery.
When the switch is closed, the energy is transformed from chemical potential energy to electric potential energy.
The electric potential energy is related to the separation of the positive and negative charges on the plates.
A capacitor can be described as a device that stores energy as well as charge.
Section 26.4

## Slide 17: Energy Stored in a Capacitor
Assume the capacitor is being charged and, at some point, has a charge q on it.
The work needed to transfer a charge () from one plate to the other is
The total work required is the area of the shaded rectangle.
The total work required is
Section 26.4

## Slide 18: Energy, cont
The work done in charging the capacitor appears as electric potential energy U:
This applies to a capacitor of any geometry.
The energy stored increases as the charge increases and as the potential difference increases.
In practice, there is a maximum voltage before discharge occurs between the plates.
The energy can also be considered to be stored in the electric field.
For a parallel-plate capacitor, the energy can be expressed in terms of the field as
U = ½ (εoA/d) (E2d2) = ½ (εoAd)E2.
It can also be expressed in terms of the energy density (energy per unit volume)
uE = U/Ad = ½ εoE2.
Section 26.4

## Slide 19: Capacitors with Dielectrics
A dielectric is a non-conducting material that, when placed between the plates of a capacitor, increases the capacitance.
  Dielectrics include rubber, glass, and waxed paper
With a dielectric, the capacitance becomes
C = κCo
If the same charge is kept , the potential difference is reduced .
  The capacitance increases by the factor κ when the dielectric completely fills the region between the plates.
  κ is the dielectric constant of the material.
If the capacitor remains connected to a battery, the voltage across the capacitor necessarily remains the same.
If the capacitor is disconnected from the battery, the capacitor is an isolated system and the charge remains the same.
Section 26.5

## Slide 20: Dielectrics, cont
For a parallel-plate capacitor,
C = κ (εoA) / d
In theory, d could be made very small to create a very large capacitance.
In practice, there is a limit to d.
  d is limited by the electric discharge that could occur though the dielectric medium separating the plates.
For a given d, the maximum voltage that can be applied to a capacitor without causing a discharge depends on the dielectric strength of the material.
Section 26.5
Dielectrics provide the following advantages:
  Increase in capacitance
  Increase the maximum operating voltage
  Possible mechanical support between the plates
    This allows the plates to be close together without touching.
    This decreases d and increases C.
Emax ~ 1 V/m.
If E > Emax, break down

## Slide 21: Some Dielectric Constants and Dielectric Strengths

## Slide 22: Types of Capacitors – Tubular, oil filled and electrolytic (Optional)
Metallic foil interlaced with thin sheets of paraffin-impregnated paper or Mylar. The layers are rolled into a cylinder to form a small package for the capacitor.
High-voltage capacitors. A number of interwoven metallic plates are immersed in silicon oil.
Variable capacitors consist of two interwoven sets of metallic plates. One plate is fixed and the other is movable (area changes). Contain air as the dielectric. C varying from 10 to 500 pF.
Section 26.5

## Slide 23: Electric Dipole (Optional)
An electric dipole consists of two charges of equal magnitude and opposite signs.
d
The charges are separated by d.
The electric dipole moment () has a magnitude of p ≡ qd
An electric field can cause a dipole to change its orientation.

## Slide 24: Polar vs. Nonpolar Molecules (Optional)
Before we apply electric field,
  a molecule with a net dipole moment is called a polar molecule.
  a molecule without a net dipole moment is called a nonpolar molecule.
A water molecule is an example of a polar molecule.
The center of the negative charge is near the center of the oxygen atom.
The x is the center of the positive charge distribution.
The dipole moment is pointing downward
Example:
Water molecule

## Slide 25: Dielectrics with polar molecules – An Atomic View
The polar molecules that make up the dielectric are modeled as dipoles.
The molecules are randomly oriented in the absence of an electric field.
An external electric field is applied - > torque
The molecules partially align with the field.
    The degree of alignment depends on temperature and the magnitude of the field.

## Slide 26: Dielectrics with nonpolar molecules – An Atomic View, 2
If the molecules of the dielectric are nonpolar molecules, the electric field produces some charge separation.
This produces an induced dipole moment. The effect is then the same as if the molecules were polar.
Section 26.7
As a result, an external field can polarize the dielectric whether the molecules are polar or nonpolar.
The charged edges of the dielectric act as a second pair of plates producing an induced electric field in the direction opposite the original electric field.

## Slide 27: Induced Charge and Field
The electric field due to the plates is directed to the right and it polarizes the dielectric.
The net effect on the dielectric is an induced surface charge that results in an induced electric field.
If the dielectric were replaced with a conductor, the net field between the plates would be zero.
Section 26.7